## Slide 1: Library Characterization
Divya Akella, Abhishek Roy
University of Virginia

## Slide 2: Motivation for std. cell characterization
Create high quality models of a std. cell library which can accurately emulate circuit behavior
These models can be used for several digital design/synthesis tools for different purposes

## Slide 3: What is a library characterizer
Creates electrical views (timing, power and signal integrity/noise) in industry standard formats such as Synopsys liberty (.lib) format, .cdb format for Noise models etc.
Conventionally, it only requires foundry device models and extracted cell netlists ( for better accuracy, noise models) to create all the required electrical views
By automating the process for generating views, it ensures that the library’s functional, timing, power and signal integrity values are accurate and complete to avoid potential chip failures

## Slide 4: Library characterization packages
The tools/information required are
  Analog simulator (Hspice, Spectre etc.)
  Netlist of the cells (extracted esp. if creating noise models or using advanced/newer processes. For timing only, pre-layout is OK if using 130nm)
  Device models from the foundry
  An idea of the timing arcs if using custom cells (I/Os, level shifters, new flip-flop architecture etc.)
Vendors
  Synopsys SiliconSmart
  ELC
  Liberate (Cadence)

## Slide 5: Timing model formats
NLDM : Non-linear delay model
  Input transition vs. capacitive load Look-up Table (LUT) for picking delays. Similar LUTs for setup/hold etc.
  Constant voltage based. No effect of IR-drop or Ldi/dt effects on cell delay modeled.
  Reasonably accurate for 90nm and older. Not accurate for newer technologies (65nm and below)
Current source modeling
  CCS (Composite current source) and ECSM (Effective current source model)
  Current-based measurements to determine metrics such as input-capacitance of std-cells etc.
  More accurate estimates of interconnect impedance and its impact on the overall delay.
  Models effects of IR-drop and LdI/dt effects on cell delay
  Recommended for use in 65nm and below but more complex and time consuming to generate

## Slide 6: Timing Arcs
Can be delay arcs (most common. Present in both combinational and sequential cells) or constrained arcs (flip-flops, latches etc.)
Timing arcs have a start-point (input,output,inout pin) and an end-point (output,inout pin)
  Not valid for constrained timing arc such as setup,hold,recovery, removal which can be between two inputs ( e.g; clock and data)
If cell characterization tool is unable to identify the cell, timing arc generation and creation should be understood in detail

## Slide 7
Tool Details
Cadence Liberate | /app3/cadence/LIBERATE161/bin/liberate
Pre-requisites | /var/home/ece/bin/cadence2011 /var/home/ece/bin/synopsys-setup
Tutorial | /var/home/bengroup/libs/characterization_tutorial
Sample cell | /var/home/bengroup/libs/characterization_tutorial/sample
Command | /app3/cadence/LIBERATE161/bin/liberate char.tcl > char.log Or just: tcsh runfile
Tutorial
How to run?

## Slide 8
Characterization flow
Set parameters
Load templates
Load netlists and models
Characterize library
Write libary

## Slide 9
Setup Tcl Script: char.tcl
Set different variables | 
set lib_name BUFX2TS_STARVE | Specifies the name of the resultant library
set_operating_condition -voltage 0.5 -temp 27 | Defines default process, temperature and voltage to be used for library creation. Automatically identifies VDD as power and 0, GND, and VSS as ground
set_vdd -type primary VDD 0.500 set_vdd –type primary VSS 0 | Identify name(s) of ground and power nets. Can be used to override defaults set by above.
set_pin_vdd -supply_name VDD3 BUFX2TS_STARVE VREF 0.200 set_pin_gnd -supply_name VSS BUFX2TS_STARVE VREF 0 | Associate a pin of a cell with a particular supply domain. Particularly useful on cells that have multiple power and ground.
Load template for each cell | 
source template_ibm130.tcl | Load template
define_template -type power \ -index_1 {0.129 0.250 0.499 0.992 } \ -index_2 {0.004 0.016 0.08} \ power_template_4x3 | Defines a template to be used for characterization for delay, power etc.

## Slide 10
define_cell \ -input {A VREF} -output {Y} -pinlist {A VREF Y} -delay delay_template_4x3 –power power_template_4x3 BUFX2TS_STARVE | Defines how a cell is to be characterized.
define_arc \ -vector "F0F" -when "!VREF" -related_pin {A} \ -pin Y BUFX2TS_STARVE | Specifies a user-defined arc to override automatic arc determination by Liberate.
Load models and netlists | 
set spicefiles include.scs lappend spicefiles BUFX2TS_STARVE.scs | Set the path to models and netlists
read_spice -format spectre $spicefiles | Read the netlists
Characterize the library | 
char_library -cells ${cells} -extsim hspice | Command to characterize
Characterize the library | 
write_library -user_data user_data.lib -overwrite {lib_name}.lib | Write into the library User_data.lib : you can make the .lib look like this

## Slide 11
Recommendations
Read the manual: /app3/cadence/LIBERATE161/doc/liberate/*
Get started on characterization to learn: /var/home/bengroup/libs/characterization_tutorial/sample
Other useful documentation
  Synopsys Liberty (.lib) format : https://people.eecs.berkeley.edu/~alanmi/publications/other/liberty07_03.pdf
  Eric Brunvand, “Digital VLSI chip design with cadence and synopsys CAD tools”